## Slide 1: First Responder Hazmat Awareness Level Training
UNIT 1 - “Preparation”
Notes: 1
1

## Slide 2: Unit Objectives
Define Hazardous Materials
Identify the role of the Awareness Level First Responder
Identify the Awareness Level Response Goals
Notes: 2
2

## Slide 3: Hazardous Materials
Defined in numerous ways
U.S. Department of Transportation (USDOT)
U.S. Environmental Protection Agency (USEPA)
U.S. Occupational Safety and Health Administration (OSHA)
Simplified Definition
Extremely Hazardous Substances
Notes: 3
3

## Slide 4: Hazardous Materials Incidents
“Haz-Mat” incidents are unique incidents. They require specialized protective measures not normally available to first responders AND they demand a different operational approach!
Notes: 4
4

## Slide 5: Public Safety “Duty to Act”
Public safety responders have a “Duty to Act”.
Your level of involvement is defined by your employer’s Emergency Response Plan (ERP).
The actions you are expected to take should be in Standard Operating Procedure format.
NEVER exceed your level of training and protection!
Notes: 6
6

## Slide 6: North American Emergency Response Guidebook
Your tool for success.
Purpose:
  An aid for identification of the material involved.
  Outlines basic initial actions.
  Recommends protective action areas.
  Serves as an initial incident safety plan.
Notes: 8
8

## Slide 7: Five Levels of Training
First Responder Awareness Level
First Responder Operational Level
Hazardous Materials Technician
Hazardous Materials Specialist
Hazardous Materials Incident Commander
Notes: 11
11

## Slide 8: Operational Modes
Awareness and Operational level responders take DEFENSIVE actions.
Technicians and Specialists take OFFENSIVE actions.
The Incident Commander coordinates the response and is ultimately responsible for safety.
Notes: 12
12

## Slide 9
First Responder Awareness Level Training
Unit 2 - “Hazard Identification”
Notes: 1

## Slide 10: Unit 2 - Hazard Identification
  Unit Objectives:
  - Identify the six clues to the presence of hazardous materials.
  - Identify the various hazard classes of hazardous materials.
  - Describe ways in which you can determine the specific identity of a hazardous material.
Notes: 2

## Slide 11: Clue #1-Occupancy and Location
Specific occupancy or general area
Fixed facilities
Five modes of hazardous materials transportation
Drug lab considerations
Notes: 2

## Slide 12: Clue # 2 - Container Shape and Size
Classifications
  Portable, fixed or transportation
Pressure
  Non-pressurized, low or high pressure
Vapor Pressure and Storage
  The higher the pressure, the greater the potential for catastrophic failure
Notes: 6

## Slide 13: Clue # 3 - Placards and Labels
Placards and their limitations
  Not always required
  The 1000 pound rule
Placards and labels used for transport are based upon DOT Hazard Class
Nine Hazard Classes
  Subdivided into divisions
Notes: 7

## Slide 14: Hazard Classes
Hazard Class 1 - Explosives
Hazard Class 2- Gases
Notes: 8

## Slide 15
Hazard Class 3-
Flammable/Combustible Liquids
Hazard Class 4- Flammable Solids
Notes: 9

## Slide 16
Hazard Class 5- Oxidizers and Organic Peroxides
Hazard Class 6- Poisonous and Infectious Substances
Notes: 10

## Slide 17
Hazard Class 7- Radioactive Materials
Hazard Class 8- Corrosive Materials
Notes: 13

## Slide 18
Hazard Class 9-
Miscellaneous Hazardous Materials
Notes: 16

## Slide 19: Clue # 4 - Shipping Papers and Facility Documents
Notes: 18

## Slide 20: Material Safety Data Sheets (MSDS)
Required to be maintained by the Federal Hazard Communication Standard and The Florida Right-to-Know Law
Found at fixed facilities
Provides a variety of information
Emergency Response Plans (ERP)
Emergency Action Plans (EAP)
Notes: 19

## Slide 21: Clue # 5 - Markings and Colors
Container colors are not always standardized
UN/NA identification numbers
NFPA 704 Diamond
Military markings
Notes: 20

## Slide 22
Notes: 21

## Slide 23: Clue # 6 - Human Senses
RISK
LEVEL
High
Low
Taste Sound Sight Smell Touch
Notes: 22

## Slide 24: Methods of Identification
Once you recognize, try to identify
Location of material name
  Shipping papers
  MSDSs (fixed facilities)
  Facility Pre-Plans
  Employees and bystanders
If you cannot safely identify, try to classify the material into a hazard class
Notes: 23

## Slide 25: Unit Summary
Goals of recognition and identification
  Recognize, Classify, Identify
Six clues to the presence of hazardous materials
  Occupancy and location, container shape and size, placards and labels, shipping papers and facility documents, markings and colors, the human senses
There are nine general classes of hazardous materials
Notes: 24

## Slide 26: First Responder Awareness Level Training
Unit 3 - “Taking Control”
Notes: 1
1

## Slide 27: Objectives
Identify the procedures for initiating your Emergency Response Plan.
Identify the proper procedures for implementing protective action distances.
Take actions necessary to properly isolate the incident.
Notes: 2
2

## Slide 28: ERG Book
North American Emergency Response Guidebook
Familiarize yourself
Download App
Notes: 3
3

## Slide 29: Steps for Proper Use of the ERG
Recognize & Identify Hazardous Materials
  Name
  Four digit ID number
  Placard description
Look up the guide page number
Take basic protective actions according to the guide page
Initiate isolation and evacuation according to protective action distances
Notes: 4
4

## Slide 30: Basic Protective Actions
Your approach
Your main objectives
  Isolate
  Protect by preventing contamination
  Initiate your Emergency Response Plan (Notify)
Notes: 5
5

## Slide 31: Proper Guide Page Use
Notes: 6
6

## Slide 32: Table of Protective Action Distances
Notes: 7
7

## Slide 33: Protective Action Options
Shelter in-place
  Short duration incidents
  Greater hazard to attempt to move
  Impractical to evacuate
Evacuation
  Potential for massive fire or explosion
  Long duration incidents
Notes: 8
8

## Slide 34: Emergency Response Information
Firefighting
  Definition of “Haz-Mat Fire”
  Defensive Vs. Offensive
  Role of the awareness responder
Spill / Leak Control
  Not an awareness level role
First Aid
  Remember to prevent secondary contamination
Notes: 9
9

## Slide 35: Summary
ERG provides guidelines
You can find a guide page by:
  Name, ID number or placard comparison
Basic instructions - page 1
Two indexes
Orange guide pages
Green protective action pages
Notes: 10
10

## Slide 36
THE END
Thank you and stay safe!!